TUTORIAL CHOOSING INPUT AND OUTPUT DEVICES

- Give two examples of analogue output devices

- State the conversion that takes place in the two examples given in question 1

- Give an example where each of the output devices in question 1 could be used.

- Give two examples of digital output devices

- State the conversion that takes place in the two examples given in question 4

- Give an example where each of the output devices in question 4

- Draw an label the correct symbol for

i ) an LED

ii) a torch bulb

- On your diagram of an LED show the correct connections to male the LED light.

- Explain why it is necessary to place a resistor in series with an LED.

- Draw a diagram showing how each number from 0-9 is displayed on an seven segment display.

- For each of the following devices state the most suitable output device and say whether it is analogue or digital.

  - A baby alarm system, which allows parents to hear their baby cry even when they are in another room.

  - A doorbell indicator for the deaf.

  - A remotely controlled switch for an X-ray machine

  - a power on indicator for an electronic device, such as a computer.

  - an easily interpreted display for a measuring instrument, such as a joulemeter.

  - A remotely controlled bolt which allows smoke doors to close in case of a fire.

- Choose a suitable INPUT device for each of the following applications

  - a light meter for a camera.

  - a public address system

  - a temperature control for an aquarium

  - a circuit to switch on street lamps when it becomes dark

  - a speed controller for an electric motor.

  - an electronic thermometer to measure the temperature of a furnace.

  - a sunshine recorder.

- A thermistor has a resistance of 200  at 20 C. What is the current when it is connected to a 10 volt supply?

  - If the current increases to 0.1 A when its temperature is increased to 100 C what is its resistance at 100 C?

- This table shows how the current in a thermistor depends on its temperature when it is connected to a 10V supply.

Copy and complete the table

| Temperature (C) | Current (A) | Thermistor resistance () |
| --- | --- | --- |
| 0 | 0.1 |  |
| 50 | 0.2 |  |
| 100 | 0.3 |  |
| 200 | 0.4 |  |

TUTORIAL CHOOSING INPUT AND OUTPUT DEVICES

- Give two examples of analogue output devices

- State the conversion that takes place in the two examples given in question 1

- Give an example where each of the output devices in question 1 could be used.

- Give two examples of digital output devices

- State the conversion that takes place in the two examples given in question 4

- Give an example where each of the output devices in question 4

- Draw an label the correct symbol for

i ) an LED

ii) a torch bulb

- On your diagram of an LED show the correct connections to male the LED light.

- Explain why it is necessary to place a resistor in series with an LED.

- Draw a diagram showing how each number from 0-9 is displayed on an seven segment display.

- For each of the following devices state the most suitable output device and say whether it is analogue or digital.

  - A baby alarm system, which allows parents to hear their baby cry even when they are in another room.

  - A doorbell indicator for the deaf.

  - A remotely controlled switch for an X-ray machine

  - a power on indicator for an electronic device, such as a computer.

  - an easily interpreted display for a measuring instrument, such as a joulemeter.

  - A remotely controlled bolt which allows smoke doors to close in case of a fire.

- Choose a suitable INPUT device for each of the following applications

  - a light meter for a camera.

  - a public address system

  - a temperature control for an aquarium

  - a circuit to switch on street lamps when it becomes dark

  - a speed controller for an electric motor.

  - an electronic thermometer to measure the temperature of a furnace.

  - a sunshine recorder.

- A thermistor has a resistance of 200  at 20 C. What is the current when it is connected to a 10 volt supply?

  - If the current increases to 0.1 A when its temperature is increased to 100 C what is its resistance at 100 C?

- This table shows how the current in a thermistor depends on its temperature when it is connected to a 10V supply.

Copy and complete the table

| Temperature (C) | Current (A) | Thermistor resistance () |
| --- | --- | --- |
| 0 | 0.1 |  |
| 50 | 0.2 |  |
| 100 | 0.3 |  |
| 200 | 0.4 |  |