POTENTIAL DIVIDERS (a difficult bit!)

# Formula for a series circuit

In a SERIES circuit the current through each resistor is the same. To find the current use the formula:

We already know that IT is the same as the current going through R1, R2, R3 etc.  So to find V1, V2, V3, use:

As IT is the same

To find the voltage across resistors you do not need to work out the current.

Either work out by ratios (quick if you can do it but costly if it goes wrong!)

EITHER:

- Summarise

VS = 12 V, R1 = 90 (, R2 = 30 (

V1 = ?, V2 = ?

Find RT = R1 + R2

RT = 90 + 30 = 120 (

- Find V1

- Find V2

- Check

Vs = V1 + V2 = 9 + 3 = 12 V	☺

OR:

- Summarise

VS = 12 V, R1 = 90 (, R2 = 30 (

V1 = ?, V2 = ?

- Find RT

Find RT = R1 + R2

RT = 90 + 30 = 120 (

- Find IT

- Find V1

- Find V2

- Check

Vs = V1 + V2 = 9 + 3 = 12 V	☺

The third method that you can use now appears to be most popular

It is the method used in the Virtual Higher Course that you can try out for yourselves.

The formula is given below.

VOLTAGE DIVIDERS

FIND THE VOLTAGE DROP ACROSS BOTH RESISTORS.

1a) 3V, 9V		b) 8V, 2V,		c) 6V, 18V

2a) 2.5V, 0.5V		b) 0.375V, 1.125V	c) 3.6V, 2.4V

3a) 0.5V, 1V		b) 4.5V,1.5V		c) 9V, 3V

# Text boxes

R3

R2

R1

V3

V2

V1

VS

I

V2

12 V

90 (

30 (

4.7 (

14.1 (

10 V

0 V

80 (

20 (

24 V

0 V

2 k(

6 k(

3 V

0 V

500 (

100 (

1.5 V

0 V

25 (

75 (

6 V

0 V

3 M(

2 M(

1.5 V

0 V

5 (

10 (

6 V

0 V

24 (

8 (

12 V

0 V

900 (

300 (

24 V

0 V

2 k(

6 k(

18V

6V

6 V

0 V

24 (

8 (

1.5V

4.5V

1.5 V

0 V

5 (

10 (

1V

0.5V

12 V

0 V

900 (

300 (

3V

9V

6 V

0 V

3 M(

2 M(

2.4V

3.6V

1.5 V

0 V

25 (

75 (

0.375V

1.125V

3 V

0 V

500 (

100 (

0.5V

2.5V

10 V

0 V

80 (

20 (

2V

8V

12 V

0 V

4.7 (

14.1 (

9V

3V