INPUT, PROCESS, OUTPUT DEVICES AND THEIR USES

The three parts of any electronic system are INPUT( PROCESS( OUTPUT

| Name of device | Input Process Output | Symbol | Energy change | Uses |
| --- | --- | --- | --- | --- |
| Loudspeaker | O |  | electrical(sound | In CD Player, tannoy, public address system, karaoke machine |
| Motor | O |  | electrical(kinetic | washing machine, car wiper motor, food processor, vacuum cleaner |
| Bell | O |  | electrical(sound | door bell, fire bell |
| Buzzer | O |  | electrical(sound | door warning |
| Relay | O |  | electrical(kinetic | switching on high voltage equipment eg control panels |
| Solenoid | O |  | electrical(kinetic | central locking, fire doors |
| LED | O |  | electrical(light | analogue- tuner indicator on radio digital-on/off power indicators |
| Lamp | O |  | electrical( heat & light | analogue-atmospheric lighting, digital-table lamp |
| 7 segment display | O |  | electrical(light | radio alarm clock display, video player display |
| Microphone | I |  | sound(electrical | tannoy, public address system, karaoke machine |
| Thermocouple | I |  | heat(electrical | kiln thermometer |
| Solar Cell | I |  | light(electrical | power supply for a calculator, solar powered torch |
| Thermistor | I |  | heat(electrical | thermometer for an aquarium |
| Light Dependent Resistor | I |  | light(electrical | burglar alarms, automatic drive lights |
| Capacitor (& resistor) | I |  |  | pedestrian crossing patrols |
| Potentiometer | I |  |  | volume control in a stereo, boost control in a vacuum cleaner |
| Switch | I |  |  | on a table lamp |
| Transistor | P |  | no energy change | SWITCH >0.7V |
| MOSFET | P |  | no energy change | SWITCH 2 V |

LDR is short for Light Dependent Resistor- remember it as  Light Drops Resistance

. Some teachers use the term LURD- Light Up Resistance Down, and for a Thermistor (a temperature dependent resistor) TURD- Temperature Up Resistance Down.