# ELECTRICITY

Appliances	use batteries or electrical mains as their supply of electrical energy.  They all change electrical energy into another form e.g. hair dryer.  Electrical energy -> kinetic and heat energy.

Power rating	the rate at which appliances convert electrical energy into other forms.

Watts	Unit of Power

How converted electrical energy is measured.

High power	found on appliances which produce heat  e.g. a toaster

Rating

Low power   	found on appliances which produce little heat  e.g. sewing

Rating	machine

Flex	used when connecting appliance to socket.

Flex should be	thick enough to carry the current required by the appliance.

covered with fabric if it is to be bent a lot.

heat resistant.

Either 2 core or 3 core depending upon whether or not the appliance needs an earth wire.

Plug	used to connect the flex to the socket.

Can have 2 or 3 wires connected to it.

Fuse	the fuse is to protect the flex.  Too high a current through the flex and the fuse will blow and cut off the electricity supply.

P=IV	formula used to calculate the exact current an appliance requires.

Earth wire	used to prevent a faulty appliance remaining live.

Double  	 used on appliances that only have a live and neutral wire, do

Insulation	not have any conducting parts which can be touched.

.

Batteries	supply direct current (d.c.)

Mains	supply alternating current (a.c.)

Average 	230V

Mains Value

Peak voltage	the maximum voltage reached which is about 340V

Conductor	a material which allows electricity to flow

Current	the flow of electricity

Electrons	negative charges in (of) electricity.

Flow	electrons flow from the negative to the positive.

Charge	current x time (Q = lt)

Coulombs	Charge is measured in coulombs (C)

Time	time is measured in seconds (s)

Circuit 	see end

symbols

Ammeters	in a circuit ammeters are always connected in series to measure the current through a component.

Voltmeters	in a circuit voltmeters are always connected in parallel to measure the voltage across a component.

Resistance	resistance is what a component has when it opposes the flow of current around a circuit.  Resistance is a measure of how hard it is for current to flow.  The harder it is for current to flow the harder it is for current to flow the higher the resistance.

R in series	In a series circuit the resistance

Resistance is measured in ohms

As resistance increases, current decreases

Voltage	current x resistance V = 1R

Variable	the resistance of a variable resistor is changed by alternating

resistors	 its length – longer the length, the more resistance it has.

Power	energy 		P = E   The rate at which Energy is used.

Time                      t

Power		measured in Watts i.e. 1 watt = 1J/s

Time		measured in seconds

Energy		measured in joules

The units of power is also equal to joules per second.

power		= current x voltage   P = lV

Filament	ordinary light bulbs used in the home.  The energy is changed Lamps		in the filament.  These bulbs produce lots of heat as well as

light

Fluorescent	a high voltage across the gas makes it produce rays which

Lamps	 causes a coating on the inside of glass tubes to produce light.  The energy change occurs in the gas.

Series	only one path for the current to flow through components and

Circuits	 back to cell or battery.

Parallel circuit	  a choice of routes.  A circuit where the current splits up and travels down different branches.

In a series	current is same through all components I =I1 =I2 =I3  but the supply voltage is split between the components in the circuit V =V1 +V2 +V3

In parallel 	the voltage is the same across the supply V =V1 =V2 =V3  and all the resistors

Circuit	but the current leaving the supply splits between the three resistors. I =I1 +I2 +I3

Ohm meter	can be used to test for open and short circuits.

Open circuit	gives an infinite resistance.  When there is a break in the circuit.

Short circuit	gives zero resistance when

Continuity	is used to test open circuits.  Can be in many forms.  You can

Tester	test the resistance using an ohmmeter, test the current with an ammeter, test with a light bulb.

Adding

Resistors in	use the formula

parallel	                          Parallel

Resistors in

Series	R=R1 +R2 +R3

Consumer 	a fuse box in the home

Unit

Circuit beaker	- in consumer units circuit breakers take place of fuse.

The ring main	- the special parallel circuit used to connect all the power sockets in a house together.  Protected by 30A fuse.

Lighting 	not a ring circuit but a cable connecting all ceiling lights in

Circuits	 parallel.  This is protected by a 5A fuse.

Units of 	the amount of energy a householder uses is measured in units.

Energy

Kilowatt-	Units of energy used in calculating the electricity and gas

Hours	used in the home are measured in kilowatts hours (kWh)

Units used	The way energy used in calculating power x time. (power must be kilowatts and time is in hours)

Magnetic 	all magnets have a magnetic field around them.

Fields	- there is also a magnetic field around any wire which has an electric current flowing through it.

Electromagnet	 - a wire, with a current flowing through it, wrapped around an iron core.  Has the advantage that it can be switched on or off.

Carbon 	current is fed into the coil by the carbon brushes.  We use

Brushes	carbon because it wears away and protects the commutator.

Commutator	the terminals at the end of the coil works with the brushes to allow current into the coil and allows the direction of the current to change every half a turn.