INPUT, PROCESS, OUTPUT DEVICES AND THEIR USES

The three parts of any electronic system are

INPUT( PROCESS( OUTPUT

| Name of device | Input Process Output | Analogue Digital | Symbol | Energy change | Uses |
| --- | --- | --- | --- | --- | --- |
| Loudspeaker | output | analogue |  | electrical(sound | In CD Player, tannoy, public address system, karaoke machine |
| Motor | output | analogue |  | electrical(kinetic | washing machine, car wiper motor, food processor, vacuum cleaner |
| Bell | output | digital |  | electrical(sound | door bell, fire bell |
| Buzzer | output | digital |  | electrical(sound | door warning |
| Relay | output | digital |  | electrical(kinetic | switching on high voltage equipment eg control panels |
| Solenoid | output | digital |  | electrical(kinetic | central locking, fire doors |
| LED | output | both! |  | electrical(light | analogue- tuner indicator on radio digital-on/off power indicators |
| Lamp | output | both! |  | electrical( heat & light | analogue-atmospheric lighting, digital-table lamp |
| 7 segment display | output | digital |  | electrical(light | radio alarm clock display, video player display |
| Microphone | input | analogue |  | sound(electrical | tannoy, public address system, karaoke machine |
| Thermocouple | input | analogue |  | heat(electrical | kiln thermometer |
| Solar Cell | input | analogue |  | light(electrical | power supply for a calculator, solar powered torch |
| Thermistor | input | analogue |  | heat(electrical | thermometer for an aquarium |
| Light Dependent Resistor | input | analogue |  | light(electrical | burglar alarms, automatic drive lights |
| Capacitor (& resistor) | input | analogue |  |  | pedestrian crossing patrols |
| Potentiometer | input | analogue |  |  | volume control in a stereo, boost control in a vacuum cleaner |
| Switch | input | digital |  |  | on a table lamp |
| Transistor | process | digital |  | no energy change | SWITCH >0.7V |
| AND gate | process | digital |  | no energy change | various circuits see e.g. in notes |
| OR gate | process | digital |  | no energy change | various circuits see e.g. in notes |
| NOT gate (inverter) | process | digital |  | no energy change | various circuits see e.g. in notes |
| Amplifier | process | analogue |  | no energy change | to increase the signal in a radio and TV |

LDR is short for Light Dependent Resistor- remember it as  Light Drops Resistance